# A PROPOSAL FOR

EVALUATION OF THE INFLUENCE OF WETLANDS ON THE WATER QUALITY OF UPPER KLAMATH LAKE AND THE FEASIBILITY OF REESTABLISHING WETLAND-LAKE CONNECTIONS

## Prepared for

#### The Bureau of Reclamation

U. S. Department of the Interior

Klamath Basin Area Office

Klamath Falls, Oregon

## Prepared by

#### The Center for Lakes and Reservoirs

Environmental Sciences and Resources

Portland State University

Portland, Oregon

October 8, 2001

# A PROPOSAL FOR

EVALUATION OF THE INFLUENCE OF WETLANDS ON THE WATER QUALITY OF UPPER KLAMATH LAKE AND THE FEASIBILITY OF REESTABLISHING WETLAND-LAKE CONNECTIONS

## Prepared for

#### The Bureau of Reclamation

U. S. Department of the Interior

Klamath Basin Area Office

6600 Washburn Way

Klamath Falls, OR  97603

541-883-6935

## Prepared by

#### The Center for Lakes and Reservoirs

Dr. Mark Sytsma, Director

Stan Geiger, Project Manager

Environmental Sciences and Resources

Portland State University

Post Office Box 751

Portland, Oregon 97207-0751

503-725-3833

### Table of Contents

## Project Background

## Project Understanding

## Objectives

## Scope of Work

Phase I

Element A:  Characterize the influence of remaining wetlands in UKL on the seasonal quality of the lake water

Element B:  Determine the influence of marsh effluents on the development of Aphanizomenon-flos aquae blooms

Phase II

Element A:  Develop plan to reassociate areas intended for wetland restoration behind the dikes at UKL with the lake

Phase III

## Schedule and Budget

## Center for Lakes and Reservoirs Qualifications for Project

## Project Team Members and Management

## References

## Attachments

- S. Geiger 2001 paper Reassociating wetlands with Upper Klamath Lake to improve water quality.  Presented at Klamath Basin Fish and Water Management Symposium, Arcata, California, May 22-25, 2001 and at the Oregon Lakes Association meeting, Portland, Oregon September 21, 2001.

- Vitae of principal investigators

PROJECT BACKGROUND

The Bureau of Reclamation (Reclamation) is developing an Environmental Impact Statement (EIS) for the long-term operation of the Klamath Project.  Reclamation’s recent Biological Assessment of the Klamath Project’s continuing operations on the endangered Lost River sucker and the shortnose sucker (2001), and the U. S. Fish and Wildlife Service (USFWS) Biological Opinion responding to the Reclamation BA, both note the significant loss of wetlands from the Upper Klamath Lake (UKL) basin as a major factor in the decline of sucker habitat.  The USFWS reasonable and prudent alternative (RPA) to Reclamation’s proposed management plans in its BA directs Reclamation to maintain higher than historical lake levels as the primary strategy to improve water quality in the lake.  This RPA can divert attention from the valuable role wetlands can have in improving lake quality, which is alluded to in both the BA and the BO.  This proposal from the Center for Lakes and Reservoirs (CLR) at Portland State University, provides various specific initiatives for reestablishing the functions of wetlands in regulating the quality of Upper Klamath Lake water.

PROJECT UNDERSTANDING

- Wetland isolation from UKL contributes to deteriorating lake quality

The paper by S. Geiger, Reassociating Wetlands with Upper Klamath Lake to Improve Water Quality, provided as Attachment A to this Proposal, provides preliminary information to support the following hypothesis:

The isolation of former wetlands from UKL by diking and draining has resulted in degraded lake water quality through severing important lake-wetland functional connections.

We propose to test this hypothesis through characterization of wetland function, modeling of wetland influences on phytoplankton production in UKL, and a series of laboratory and in-lake experiments at increasing scale.  If the hypothesis testing does not result in rejection of the hypothesis, a whole-lake experiment  may be feasible.  The hypothesis does not suggest that isolation and draining of wetlands has been the only cause of UKL decline over the past 100+ years.  It is likely that extensive logging in the watershed and cumulative contributions from agricultural use of the land have exacerbated conditions in UKL, which has been reduced in size. The hypothesis does suggest that severing of lake-wetland functional connections may have severely impaired capability of UKL to process nutrient and sediment inputs generated by human use of the watershed.

An appropriate introductory analogy for the consequences of isolation of in-lake marshes from the lake by means of diking and draining would be the removal of an appreciable portion of the liver and kidney from a human.  It appears to be commonly believed that the effect of wetland loss was subsequent agricultural discharge from the “reclaimed” 34,140 acres of farmed and ranched area and a resultant degraded lake water quality.  The work in this proposal derives its impetus from an alternative hypothesis that loss of wetland-lake functional connection by isolation and drainage are as important, if not more important, than subsequent agricultural discharges.

- Extent of wetlands in the lake once made UKL unique

The Bureau of Reclamation in its 1997 estimate of the area and volume of Upper Klamath Lake (UKL), which in this paper will include Agency Lake, has included wetlands at lake level that are seasonally inundated by fluctuating lake water levels (Basdekas 1997).  Table 1 provides an overview of how the lake has changed in area through the isolation of 34,140 acres of marsh wetland from the lake through diking and draining.

Table 1. 	The area of littoral marsh and limnetic open water of Upper Klamath Lake (including Agency Lake) before commencement of diking (~1889) and after diking, draining and UKL outlet dam at Link River [Bureau of Reclamation data].

| Condition of Lake | Lake Surface Elevation | Lake Area (Ac) |
| --- | --- | --- |
| Before Diking | Minimum (BR datum, ft) | Littoral | Limnetic | Total |
|  | 4140.0 | 20,320 (30%) | 47,400 (70%) | 67,720 |
| Before Diking | Maximum (BR datum, ft) | Littoral | Limnetic | Total |
|  | 4143.0 | 51,510 (46.2%) | 60,000 (53.8%) | 111,510 |
| After Diking and Dam | Minimum (BR datum, ft) | Littoral | Limnetic | Total |
|  | 4136.0 | 0.0 (0.0%) | 55,800 (100%) | 55,800 |
| After Diking and Dam | Maximum (BR datum, ft) | Littoral | Limnetic | Total |
|  | 4143.3 | 17,370 (22.4%) | 60,223 (77.6%) | 77,593 |

The littoral wetland area of the lake once comprised 51,510 acres (46.2%) of the total lake area of 111,510 acres at maximum pool surface elevation.  The historical records of lake fluctuation prior to construction of the Link River Dam in 1921 document the lake fluctuating between a maximum of 4143.0 ft (U. S. Bureau of Reclamation datum [~2.3 ft above the USGS NGV datum]) and a minimum of 4140.0 ft.  Following dam construction and after the last diking and draining in 1968 (Snyder and Morace 1997), the lake area at maximum pool elevation of 4143.5 ft had decreased to 77,590 acres, with littoral marsh area decreased to 17,370 acres (22.4% of the total lake area).  In other words, the lake lost 30.4% of its area, and the associated lake volume associated with this area, through diking and draining.  The in-lake wetland area was reduced by 66.3%.  In addition, there was a reduction of littoral lake volume from 82,000 ac-ft to 28,000 ac-ft; a reduction of 65.9%.  Further, the wetland area at minimum lake storage volume (4136.0 ft versus the pre-dike, pre-dam minimum of 4140.0 ft, had shrunk from 20, 320 acres to 0.0 acres (Basdekas 1997), which represents an additional seasonal loss of function.  Lowering the reef at the Link River Dam allowed more water to be withdrawn from the lake.

- Effects of in-lake wetlands potentially large

Extensive research,  conducted and reported most prominently since 1978, has described the multifaceted capacity of wetlands to alter lake water quality (e.g. Good, Whigham and Simpson 1978; Hammer 1989; Moshiri 1993, SRI/Shapiro 1994; Kadlec and Knight 1996; U. S. Environmental Protection Agency 2000; Mitsch, Horne and Nairn 2000).  UKL is unique among large  lakes in Oregon and Washington in having a high proportion of the lake area as wetland, primarily emergent marsh wetland (Table 1).  Given the extensive decomposition that occurs each year in marshes of the Klamath Basin, primarily during late fall and winter, and the resultant release of organic detritus, plant nutrients, and dissolved organic carbon compounds, the UKL wetlands are likely to influence lake function and phytoplankton production (see Godshalk and Wetzel 1978).

- Recent modeling projects ignore wetlands

Other than defining which wetlands were lost over the past 100 years (e.g. Carlson 1993, Snyder and Morace 1997), there has been no attempt to assess the function of the extensive wetland component of the lake prior to diking and draining, and, there has been no assessment of the function of the extensive wetlands that remain in the lake.  Three recent analyses of Upper Klamath Lake have excluded wetland areas and associated wetland littoral volumes from their analyses (Kann and Walker 1999; Walker 2001, and Phil Williams and Associates, Inc. 2001).  These analyses, which attempt to draw conclusions about the performance of the whole lake system from modeling of the limnetic zone of the lake, ignore the complex contributions of the 17,370 acre littoral zone of Upper Klamath Lake, the marsh wetlands in the lake that were not isolated by diking and draining.

- Reassociation of reclaimed wetlands with UKL proceeding slowly

Figure 2 shows the location of wetlands that have been drained for agricultural use and Table 2 provides information on the areas of these wetlands both in the lake, those still being farmed, and those being restored.  The present total of this intended reclaimed wetland area is 17,553 acres.  Most of this total is owned by the Bureau of Reclamation, the Bureau of Land Management and The Nature Conservancy.  The reassociation of these reclaimed wetlands with the lake is proceeding very slowly.

- Recent water management decisions for UKL could impact wetlands

Reclamation’s directive (RPA) from the USFWS to maintain higher than historical or pre-settlement water levels for UKL may provide more habitat for the sucker at the expense of wetland fauna and flora associated with wetlands and the primary vascular vegetative components of the wetlands.  This possible change in wetland hydroperiod could be construed as an extensive wetland impact subject to regulation by the Oregon Division of State Lands and the U. S. Army Corps of Engineers.  The pressure on Reclamation to develop alternative sources of water elsewhere in the UKL basin to meet its Project obligations may also have similar associated “jurisdictional” wetland impacts.  A review of the regulatory constraints associated with altering hydroperiods and severely impacting wetlands would be valuable as part of Reclamation’s attempt to provide a comprehensive environmental assessment for long-term operation of the Project.

These background considerations associated with the wetlands of UKL inform and provide direction for the objectives of this proposed project and for the individual scope elements provided in following sections.

PROJECT OBJECTIVES

The following objectives are a context for the work scope elements that follow.

- Define pre-non-native settlement wetland extent and function and the associated quality of Upper Klamath Lake (UKL);

- Define the effects of diking and draining wetlands on the quality of UKL, including wetlands at lake surface and wetlands above the lake in the UKL basin;

- Develop a strategy for and define the effects of reassociating restored wetlands with UKL, and assess opportunity for adding to inventory of restored wetlands;

- Define the present extent of submergent, littoral wetlands, the potential for their development, and their influence on UKL water quality;

- Assess the effect on wetlands in the lake, and behind the dikes, of altering lake water elevations to improve sucker habitat;

- Assess the effects on wetlands of proposed water storage projects;

- Assess the effect of wetland and agricultural lands effluents, especially decompositional products, on the quality of UKL water and development of Aphanizomenon flos-aquae blooms;

- Assess the cumulative effect of reassociating wetlands and optimizing wetland functions for improvement of UKL water quality.

## SCOPE OF WORK

PHASE 1:  December 2001-November 2002

Element A:  Characterize the influence of remaining wetlands in UKL on the seasonal quality of the lake water

## Rationale for Work Element and Tasks

- Previous wetland studies were preliminary to defining influence

There are two previous Reclamation projects (1992-1994), Upper Klamath Marsh and Hanks Marsh, that sampled the water and biota of these marsh areas in a preliminary reconnaissance mode.   The studies resulted in some information that can be used as the basis for additional and more focused sampling.  The studies were not carried out to accomplish the intent of this work element.

The initiative by the Bureau of Reclamation in 1990 to develop a water quality management plan for the Sevenmile Canal-Wood River watershed (see Campbell 1993a, 1993b) was associated with an assessment of the Upper Klamath Marsh National Wildlife Refuge (NWR) (Sartoris, Sisneros and Campbell 1993b).  The intent of the Bureau of Reclamation investigation of the lake-associated Upper Klamath NWR marsh and the diked marsh areas was to “assess and quantify the relative effects of reclaimed and undisturbed lacustrine wetlands on the eutrophication and water quality of Upper Klamath Lake” (Sartoris, Sisneros, and Campbell, 1993b).  Field work was conducted July 1991-December 1992 concurrent with other Bureau of Reclamation studies in the Sevenmile Canal-Wood River watershed; summer of 1992 was a period of severe drought in the Klamath Basin.  Only preliminary and summary reports were produced for this work (Sartoris and Sisneros, 1993; Sartoris, Sisneros, and Campbell, 1993).  Flow measurements were only made for Sevenmile Canal at its mouth and for Fourmile (West Canal) locations.  In addition, benthic macroinvertebrates, zooplankton, and limited periphyton analyses were performed.

Reclamation also funded an assessment of Hanks Marsh (Forbes 1997, Forbes, Sartoris and Sisneros 1998, and Barber, Leenheer, Noyes and Stiles, 1999).  As Table 2 indicates, there are ~17,000 acres of wetland in the lake during the seasonal fluctuations of lake water levels.  Approximately 14,000 acres of this total is the Upper Klamath Marsh NWR (north and south units) and 1,000-1,200 of this total is Hanks Marsh.  The remaining wetland areas are generally in the north end of UKL, including portions in the vicinity of Agency Lake.

- Geiger et al. (2000) studies of Upper Klamath Marsh provide conceptual approach for further marsh investigations

Geiger, Caldwell and Hollen (2000) obtained baseline data on spring flow and quality and on water quality adjacent to and within Upper Klamath Marsh NWR.  A preliminary water and nutrient (nitrogen and phosphorus) budget was developed for the north and south units of the marsh to assess potential impacts of the proposed Pelican Butte ski area project on the marsh.  Table 3 provides an estimate, based on the best available information, of the elements of the annual inflow to the marsh and the associated annual phosphorus and nitrogen loads.  A proposed approach to monitoring the condition of this large wetland unit, with emphasis on the north 14,000 acre unit, was included in the assessment.  What is shown on Figure 2 is the location of monitoring stations that would provide information on the known influences on the marsh.  Figure 3 shows the presumed flow directions into, within and out of the UKMNWR.  What is not shown are monitoring locations that would detect the influence of the marsh on the lake.  The Pelican Bay monitoring station data (Bureau of Reclamation-Klamath Tribes) were assessed in the report as one means of characterizing what the influence of the marsh on the lake might have been.

- Assessment of wetland trophic status

There are no water quality standards specific to wetlands in the State of Oregon.  Narrative standards apply to wetlands and other waters of the state, but wetlands do not appear on the Oregon Department of Environmental Quality water quality limited water body lists (i.e., the 303(d) list).  There is no widely accepted framework for assessing the trophic status of wetlands, in the same way that the trophic state of lakes can be assessed (e.g. Walker, 1995; Kann and Walker, 1999).  Since Upper Klamath Lake is considered a eutrophic lake, even hypereutrophic by some (Walker 1995), by implication since the Upper Klamath NWR marsh is “within” the lake, it could be considered a eutrophic marsh.  But this is not necessarily the case.  A marsh’s capacity to provide additional uptake of nutrients without degrading its diversity of habitats appears to be greater than that of a lake.  This interpretation is based on a variety of assessments of wetlands that function as treatment systems for diverse upland runoff types around the world (Kadlec and Knight, 1996; Moshiri, 1993; Reed, Crites, and Middlebrooks, 1995).  It is likely there are differences in trophic (enrichment) status among wetlands in the Upper Klamath Basin (e.g., the 40,000 acres draining into the Williamson River compared with the NWR marsh) that would be based on differences in water chemistry and associated organisms.  Studies have not been done in the basin to characterize wetlands in this way.  The long association of the NWR marsh and Hanks Marsh with the enriched waters of Upper Klamath Lake would be expected to be reflected in the kinds of organisms living in the marsh.  Data on the kinds of algae identified in Crystal Creek in the 1991-1992 Bureau of Reclamation assessment indicate the presence of many algae taxa that are tolerant of increased concentrations of nitrogen and phosphorus.  The algae associated with springs at the periphery of the marsh may have a different composition than the algae within the marsh itself, but the relatively high concentrations of phosphorus in spring flow (Section 2.4) may also select for species that have greater tolerance for higher nutrient concentrations.  This is suggested by the presence in February 2000 (Shapiro observations of material collected during February 8-9 water quality sampling) of Cladophora glomerata in Crystal and Malone springs and Spirogyra sp. in Harriman spring.  These are green algae species that are tolerant of elevated concentrations of nitrogen and phosphorus (Taft and Kishler, 1973).

- The importance of hydrologic setting for determination of marsh influence on UKL

The conceptual challenge of this work element is to devise a defensible approach to detecting the influence of the marsh on the lake.  Since the marsh occupies an area within the lake, the cumulative influence of external sources on the marsh, including the changing quality of the rising and falling lake as it inundates the marsh, and the influence of the marsh on adjacent or downstream waters of the lake need to be discriminated.

Hanks Marsh is somewhat simpler with respect to sources of inflow to the marsh area.  However, determining the influence of the marsh on the adjacent open water of the lake also requires the development of a hydrologic and nutrient budget.

Perhaps the least complicated marsh hydrologic setting for determining influence of marsh on water quality would be the Wood River Marsh, approximately 700 acres situated on the east side of the Bureau of Land Management (BLM) Wood River Ranch adjacent to Wood River.  Unlike the other two marsh areas, this appears to be a stream flow marsh, by location similar to once undiked marshes in the delta of the Williamson River.

- Overview of work element tasks

The approach to this work element will be to assemble all available information on the quality and function of marshes that remain in the lake, characterize the hydroperiods or hydrologic settings of each marsh, or representative marshes, develop approaches to monitoring hydrologic, chemical and biological characteristics of each marsh that will provide sufficient data for modeling, develop preliminary hydrologic and nutrient budgets, and model the function of the marshes relative to the open water areas of the lake.

##### Element A Tasks

- Data compilation and review (Post-doc/technician, graduate student, Geiger, Wells, Koch)

1a. Assemble Geographical Information System (GIS) files (primarily from Reclamation) and develop a GIS project for former and in-lake wetlands within the seasonal elevation of UKL that incorporates all available information relative to the structure and function of wetlands that would have some bearing on the influence of wetlands on lake quality.

1b. Assemble and assess the information available on UKL in-lake marsh structure and function, seasonal DOC production, and information on former marsh areas at the lake surface.

1c. Characterize marsh areas within the lake with respect to their hydrologic settings in or at the edge of the lake including the amount of survey information on marsh sediment surface elevations, to set direction for hydrologic budget development and monitoring of chemical and biological features.

1d. Review and assess the monitoring data obtained by Reclamation and the Klamath Tribes for Pelican Bay sites (which appear to be among the most heavily marsh-influenced parts of the lake) January 1990-November 1995 (chemistry) and January 1990-June 1997 (phytoplankton and zooplankton), especially noting the period of July 1991-December 1992 when Reclamation was monitoring within the north NWR unit.

1e. Prepare a literature review of strategies for monitoring wetland-lake chemical and biological influences.

1f. Evaluate existing and alternative models with respect to incorporation of wetland processes for the purpose of shaping data collection and ultimately for modeling the influence of wetlands on UKL.

- Sampling and QA/QC Plan Development (all CLR project participants)

2a. Select monitoring locations, sources of data for the development of hydrologic and chemical budgets from other on-going monitoring programs, statistical analysis approaches.

2b. Develop and obtain approval from Reclamation and the Oregon Department of Environmental Quality (DEQ) of a quality assurance plan.

- Field sampling and data analysis (Post-doc, grad student, Geiger)

Collect hydrologic, elevation, chemical and biological data on UKL wetlands according to the quality assurance plan, incorporating GPS equipment to locate and revisit sampling sites, with the support of Reclamation air boats and local laboratory analyses (e.g. Oregon Institute of Technology) where possible.

- Model wetland function (Wells, Koch, and Post-doc)

Develop a model of wetland function for input into a UKL water quality model.

- Evaluate regulatory implications of lake mangement. (Geiger)

Develop a preliminary assessment of the wetland regulatory implications associated with Reclamation’s alternative strategies for lake water level management, including an assessment of marsh trophic status relative to DEQ water quality standards.

- Project coordination and reporting (all CLR project participants)

6a. Hold monthly meetings of Center for Lakes and Reservoirs project participants

6b. Hold quarterly meetings with UKL-area collaborators to review progress and direction.

6c. Produce an annual report.

Element B:  Determine the influence of marsh effluents, in particular decomposition products, on the development of Aphanizomenon-flos aquae blooms

Rationale for Work Element and Tasks

- Aphanizomenon biomass low in marsh environments

The cyanobacterial phytoplankton species Aphanizomenon flos-aquae dominates the plankton algae assemblage in UKL through the period of May through October.  The prominence of this species, and the primary focus of past work on the planktonic algae of the open waters of the lake, has diverted attention from other algae that are present in the wetland areas of the lake and during the times of the year when Aphanizomenon is not dominant, and may even be absent.  Bureau of Reclamation funding has supported examination of only limnetic samples, with the sole exception of the Pelican Bay site, and the speciation and volumetric estimation of the species found in this open water part of the lake.  The potential influence of wetlands in the lake on the growth of Aphanizomenon flos aquae is suggested by the data on this species’ biomass at the Klamath Tribes Pelican Bay station (in the vicinity of the Upper Klamath Lake NWR) compared with its biomass at other locations (mid-north and mid lake stations of the Klamath Tribes limnological monitoring program) (Kann 1999).  Figure 3 shows the very significantly smaller Aphanizomenon biomass in the vicinity of the marsh at Pelican Bay compared with the other open lake stations.

This absence or scarcity of Aphanizomenon just downstream, at or within marsh environments has been noted by those scientists who have spent time obtaining data on marsh character.  Forbes (1997) noted the absence of Aphanizomenon except at the waters off the edge of Hanks Marsh, and Sartoris, Sisneros and Campbell (1993) noted the same in their report on characteristics of Upper Klamath Marsh National Wildlife Refuge.  Perdue et al. (1981) noted the absence of Aphanizomenon in Upper Klamath Lake at a location heavily influenced by the Williamson River.

- Experimental work on humic substances and Aphanizomenon growth suggest importance of UKL marsh decomposition products

Forbes (1997) noted the work of Kim and Wetzel (1993) in assessing the effect of dissolved humic substances, one of the products of marsh plant decomposition, on the growth of various species of algae.  A preliminary literature review indicates that a wide variety of possible mechanisms involving dissolved organic matter have been proposed to explain the effects observed on the growth of Aphanizomenon in the vicinity of Upper Klamath Lake marshes.  An incomplete list of proposed mechanisms includes:

- The effect of dissolved organic material on light availability (Havens et al 1998);

- Kim and Wetzel (1993) found that humic substances enhanced or suppressed algal growth.  Anabaena flos-aquae was inhibited by 20 mg/l of Typha humic acids while the growth of the diatom Nitzschia palea was stimulated.  Microcystis aeruginosa growth was inhibited by all, except very low (1 mg/l)  concentrations of humic acids.

- Various interactions among dissolved iron, dissolved organic matter and phosphorus (Jones et al 1993; Guildford et al 1987, Jackson and Hecky 1980);

- Various interactions between dissolved organic matter and nitrogen availability (Berman and Chava 1999; Devol et al 1984);

- Complexation of toxic metals by dissolved organic matter (Xue and Sigg 1999).

Phinney et al. (1959) tested the effects of Klamath Marsh waters on the blue-green alga Anabaena cylindrica.  They replaced one-fourth of an algal medium with Klamath Marsh water, which resulted in the death of the test algae.  When the same experiments were repeated, but with the pH raised with NaOH, algal growth was simulated.  In 1962 at Oregon State University, C. Peek, with the assistance of H. Phinney, approached the puzzle of the reasons for Aphanizomenon dominance in Upper Klamath Lake with an evaluation of the potential growth promoting qualities of humic substances (Peek 1963).  It would appear that an assessment of potential suppressing effects on Aphanizomenon from the lake of dissolved organic carbon constituents, including dissolved humic substances, from the marshes of the lake, would be a valuable contribution to an understanding of what the loss of wetlands from the lake has meant for lake quality.

A preliminary bioassay of the effects of different concentrations of marsh water on UKL water during a Aphanizomenon flos-aquae bloom was conducted by members of the CLR project team at the end of August near the Running Y Ranch Resort.  Water from the recently restored Caledonia Marsh Test Unit was used to test effects.  Triplicate controls (marsh and lake water) and tests (3) were conducted August 27-31, 2001.  Results of the bioassays are not yet available for review.

- Insufficient characterization of the organic compounds and other marsh decomposition products in UKL, or UKL tributary, water

It is not possible with the historical nutrient inflow or limnological data bases (Kann 1998, 1999), or even previous study data (e.g. Miller and Tash 1967,  Klamath Consulting 1983), to differentiate water high or low in total and dissolved organic carbon or dissolved humic substances (DHS).  The interpretation of light measurements (Secchi disk, PAR, etc.) must therefore be ambiguous in this stream and lake system where the seasonal brown color of water in Link River, and the Lower Klamath River is a signature feature.

There has been no systematic, seasonal monitoring of dissolved humic substances (DHS), or other organic decomposition products, including total organic carbon (TOC), dissolved organic carbon (DOC), tannins and lignins, or color in streams or in the lake.  There has been only one station, the Pelican Bay station, out of twelve stations sampled in the lake since 1990 (Kann 1999) that would have been in the immediate vicinity of a large wetland.  The Pelican Bay station was discontinued by the Klamath Tribes after 1995 (water quality; 1997 phytoplankton).  The data from the Pelican Bay station was excluded from the data set used to estimate lake-wide means of forms of nitrogen and phosphorus in recent attempts to develop a water and nutrient budget for the lake and a total maximum daily load for total phosphorus (Kann and Walker 1999, Walker 2001).

Recent measurements of organic carbon constituents have been made by Shapiro and Associates, Inc. related to its recent work in assisting Running Y Ranch Resort reclaim 554 acres of wetland at Caledonia Marsh adjacent to Howard Bay (see Shapiro and Associates, Inc. 2001).  Samples of water from a 94 acre reclaimed marsh test unit provided information on the dissolved organic carbon concentrations in a young marsh (first growing season 1998).  Samples of water were also obtained from Howard Bay and from pumped winter field floodwater drainage discharge.  Preliminary results are provided in Table 4.

Table 4.	Dissolved organic carbon (DOC, mg/l) concentrations at sampling stations in Howard Bay, Geary Canal Wocus Marsh pumping station, and at the wetland reclamation unit (Test Unit of 94 acres) at Running Y Ranch Resort on Caledonia Marsh 1998-2001 (Shapiro and Associates, Inc., Portland, Oregon).  All analyses were performed by Aquatic Research Inc., Seattle, Washington.

| Date | Sampling Sites | DOC (mg/l) |
| --- | --- | --- |
| Howard Bay |  |  |
| July 2, 1998 | Howard Bay-Dike | 8.97 |
| May 19, 1999 | Howard Bay-Dike | 6.61 |
| July 24, 1999 | Howard Bay-Dike | 11.90 |
| February 9, 2000 | Howard Bay-TS | 7.13 |
| May 3, 2000 | Howard Bay-HB30 | 6.06 |
| May 3, 2000 | Howard Bay-Dike | 6.14 |
| December 19, 2000 | Howard Bay-TS | 7.40 |
| December 19, 2000 | Howard Bay-140 | 7.25 |
| Geary Canal |  |  |
| February 9, 2000 | Geary Canal Pumps | 40.30 |
| May 3, 2000 | Geary Canal Pumps | 22.10 |
| January 31, 2000 | Geary Canal Pumps | 43.10 |
| January 31, 2000 | Geary Canal Pumps | 43.60 |
| Caledonia Marsh |  |  |
| July 2, 1998 | Caledonia Marsh TU | 43.10 |
| July 2, 1998 | Caledonia Marsh TU | 56.30 |
| May 19, 1999 | Caledonia Marsh TU | 93.40 |
| May 19, 1999 | Caledonia Marsh TU | 32.20 |
| July 24, 1999 | Caledonia Marsh TU | 67.60 |
| July 24, 1999 | Caledonia Marsh TU | 43.10 |
| February 9, 2000 | Caledonia Marsh TU | 42.20 |
| May 3, 2000 | Caledonia Marsh TU | 58.40 |
| January 31, 2001 | Caledonia Marsh TU | 53.50 |

Since humic carbon can comprise over 50% of the dissolved organic carbon concentrations (Perdue et al. 1981), both wetlands in the lake, reclaimed wetlands behind the dikes, and winter-flooded farm fields are large reservoirs of what may be a valuable cyanobacterial suppressant.  The loss of in-lake wetlands, which would have diffused these humic compounds differently and at different times depending on hydrologic setting, would have resulted in lower post-diking lake concentrations of dissolved humic substances.

## Element B Tasks

The following tasks are proposed to investigate the effects of marsh effluents on the growth of the dominant cyanobacteria at UKL.

- Literature review (Post-doc, graduate student, Geiger)

- 1a. Review lieterature on Aphanizomenon (A. flos-aquae), dissolved organic carbon and dissolved humic substances, marsh decomposition products and processes, and zooplankton (e.g. Daphnia) growth in marsh waters, to assist in setting direction for opportunities and mechanisms of growth suppression effects.

- 1b. Evaluate previous Oregon State University, Humboldt State University, and Reclamation bioassays (e.g. Ehinger 1993a, 1993b, 1993c and 1994), and our August 2001 bioassay results, of treating UKL water, during the Aphanizomenon flos-aquae late summer bloom, with different proportions of Caledonia Marsh restoration wetland marsh water to test effects on cyanobacterial growth in order to refine an in-situ bioassay approach.

1c. Obtain and review data on UKL marsh vegetation and agriculture crop (e.g. barley straw) decomposition products and analytical methods for measuring these products (e.g. Shapiro and Associates, Inc. data, Barber et al 1999).

- 1d. Review anecdotal comments on the absence of Aphanizomenon flos-aquae growth in marsh environments (e.g. Renne 1999, Watkins 1999, Shapiro and Associates, Inc.2000).

- Experimental design (All CLR project participants)

2a. Develop an experimental design for laboratory and in-situ bioassays to test the effects of marsh effluents, focusing on dissolved humic substances, on the seasonal growth of Aphanizomenon flos-aquae; specify associated environmental measurements (e.g. pH, DO, SpC, temp, light, nutrients, DOC, DHS, etc.) and measures of algal response (e.g. C14, chlorophyll a, biomass, species composition); and develop a quality assurance plan for the bioassays.

2b. Design experiments to investigate important ecophysiological mechanisms that regulate Aphanizomenon growth.

2c. Design sampling program to investigate causes of low Aphanizomenon abundance within marsh vegetation.

2d. Design scaled-up experiments (all CLR project participants)

If suppression effects are documented in bioassays, provide estimates of the amount of marsh decomposition products that would need to be generated annually, and during which periods, to produce suppression effects within UKL; and, develop plans for a larger-scale,  mesocosm tests of the effects of decomposition products on cyanobacterial growth.

- Conduct sampling within marshes ((Post-doc/technician, grad student, Geiger)

- Conduct sampling within marshes and where marsh water is obviously influencing adjacent open water to determine phytoplankton composition, DOC-DHS content, ph, DO, SpC and light; and, observe responses of Aphanizomenon flos-aquae in water introduced to restored marshes behind the dike to compensate for evaporation [this task is related to obtaining data on marshes described in Phase I/Element 1].

- Conduct bioassays (Post-doc/technician, grad student, Geiger, Petersen, Rueter, Henry)

Conduct seasonal bioassays (e.g. May, June, July and August), and fall-winter laboratory bioassays on cultured Aphanizomenon flos-aquae, according to quality assurance plans to determine whether specific marsh decomposition products and agricultural plant decomposition products suppresses the cyanobacterial growth and at what concentrations.

- Conduct ecophysiology experiments (Rueter, Henry)

- Conduct studies on the mechanism responsible for inhibition of Aphanizomenon growth by marsh water (Task is contingent on demonstrating the inhibitory effect in bioassays)

- Conduct mesocosm-scale experiments (Post-doc, frad student, Geiger, Petersen)

Conduct mesocosm experiments to test the effect of marsh water on phytoplankton production in UKL.

- Project coordination and reporting (all CLR project participants)

6a. Hold monthly meetings of Center for Lakes and Reservoirs project participants

6b. Hold quarterly meetings with UKL-area collaborators to review progress and direction.

6c. Produce an annual report.

Element C:  Develop plan to reassociate areas intended for wetland restoration behind the dikes at UKL with the lake

Rationale for Work Element and Tasks

- Extent of conversion of ranch and farm land to reclaimed wetland

As was noted in the Project Understanding section of this Proposal, the reassociation of the 17,553 acres of reclaimed wetlands with the lake is proceeding very slowly. The potential benefit for improving UKL quality from this restoration is large.  In an attempt to compensate for wetland losses, both the federal government and privately funded organizations have, with support of some wetland scientists (e.g. Gearheart et al. 1995), purchased former farmed and ranched wetlands areas and are reclaiming these areas as wetland.  This conversion of land from ranching and farming began in 1995 with the purchase of the Wood River Ranch on the north side of Agency Lake.

As shown in Figure 2 and Table 2, the 17,553 acres is a combination of Agency Lake Ranch (Bureau of Reclamation, 7,159 ac), the Wood River Ranch (Bureau of Land Management, 2,880 ac), the Williamson River Delta Preserve (The Nature Conservancy, 6,960 ac), and portions of Caledonia Marsh (Running Y Ranch/Resort, 554 ac).  The land surfaces of these areas to be reclaimed are generally at elevations six or more feet below maximum lake elevations.  The total investment to acquire these former wetland areas has been $19-20 million.  The cost of reclaiming and developing wetlands is additional.

- Obstacles to progress on reassociating reclaimed wetlands with UKL

It is uncertain whether the initial federal initiative to reclaim the Wood River Ranch on Agency Lake gave high priority to ultimate use of the area for water quality improvement of Sevenmile Canal and Wood River waters.  The reclamation of the delta of the Williamson River by The Nature Conservancy was no doubt seen as an ultimate benefit to fish of UKL, both suckers and trout, but restoring the functions of former wetlands for water quality improvement may have seemed less important.  The purchase of Agency Lake Ranch by Reclamation was done both for water storage and for water quality improvement.  There has been little progress in achieving a common vision regarding wetland use for water quality improvement among these three owners of most of the 17,000 acres behind dikes targeted for restoration.  In addition to the lack of a coordinated management strategy, there have been substantial permitting obstacles to achieving limited reclamation on some of these lands, not the least of which relate to water rights, cultural resource concerns, and permitting of impacts to waters of the state.

Work Element C Tasks

The goal of these tasks of this work element will be to develop a plan, in association with the owners of land being reclaimed for wetlands, that will define the role these wetlands can and will play in improving the water quality of UKL.

- Establish a reclaimed wetlands working group, comprised of representatives of the reclaimed wetland area landowners, and initially facilitated by representatives of the Center for Lakes and Reservoirs, to explore the potential role of reclaimed wetlands for water quality improvement, to share findings on wetland reclamation methods, to assess obstacles to reclamation progress, review and explore sources of funding for reclamation, and to develop a common strategy for implementing a coordinated use of reclaimed wetlands for the improvement of lake water quality.

- Assess the status of wetland reclamation, and its potential on lands targeted for reclamation, through site visits, interviews with reclamation managers, and review of all monitoring reports and data collected related to the reclamation.

- Define the extent of pollution from agricultural practices on adjacent stream or lake waters from these reclaimed wetland areas prior to conversion to wetland from best available information and supplemental analyses.

- Define the opportunity and obstacles to circulation of stream or lake water through reclaimed wetland areas for purpose of water quality improvement, including need for fish screens for protecting stream or lake fish.

- Assess the opportunity for coordinated pump discharge of winter flooding of wetland vegetation, or from flooding of transitional farm crops such as barley, into Agency Lake for potential control of Aphanizomenon by means of marsh or crop decomposition products; test the quality of water overlying decomposing marshes or crops; assess regulatory constraints on pump discharge of expected volumes and quality of discharge.

- Design small scale demonstration projects on reclaimed wetland areas to test the potential benefit of circulating stream or lake water through wetland areas for water quality improvement; obtain review of the proposed projects by landowners; devise funding opportunities for facilitating these projects; and define a process for obtaining final approvals for implementation.

- Design monitoring programs for the small-scale demonstration projects that will provide data and analytical techniques to assess the seasonal performance of wetlands for water quality improvement; develop a quality assurance plan for the proposed monitoring program.

- Estimate the potential benefit on lake water quality from the full-scale operation of the reclaimed wetland areas through pumped discharge of winter-time flood waters and summer recirculation of stream and lake water, with estimated costs of development, including pumps and fish screens, and operation costs, and, an assessment and permitting plan to facilitate rapid implementation.

Element D:  Using information from Element A, characterize the pre-settlement, pre-diking-draining extent and function of wetlands in UKL

Element E:  Develop a proposal to increase water production from the Klamath Forest Marsh area, and provide a preliminary assessment of the effects of this project on publicly and privately owned marsh lands and wetlands

## PHASE 2

Element A:  Implement plan for small-scale reassociation of areas intended for wetland restoration behind the dikes at UKL with the lake

Element B:  Implement plan to scale up in-lake test of influence of marsh decomposition products on growth of Aphanizomenon flos-aquae

Element C:

## PHASE 3

## Element A:  Implement full-scale reassociation of reclaimed wetlands with UKL

## Schedule and Budget

## Center for Lakes and Reservoirs Qualifications for Project

## Project Team Members and Management

Mark D. Sytsma, Ph.D.

Director, Center for Lakes and Reservoirs
Environmental Sciences and Resources
Portland State University

Dr. Mark Dr. Sytsma has over 20 years experience in applied limnology and aquatic biology and management. He received his Ph.D. in Ecology from UC-Davis in 1992.  Since 1994, he has been on the faculty at Portland State University where he is an Associate Professor of Environmental Sciences and Resources and director of the Center for Lakes and Reservoirs (CLR).  The CLR was established by the Oregon legislature to address lake, aquatic weed, and invasive aquatic species issues in the state. Dr. Sytsma is a past-president of the Western Aquatic Plant Management Society, is a founding member and coordinator of the Columbia Aquatic Nuisance Species Initiative, and is on the executive committee of the Western Regional Panel on Aquatic Nuisance Species and the Oregon Invasive Species Council. Dr. Sytsma has received over $1.5 million in grants and contracts in the past three years for work on aquatic ecosystem management. Current projects include development of lake nutrient criteria and an inventory of lakes in EPA Region 10, survey of invasive species in the lower Columbia River, regional coordination of aquatic nuisance species management, technical assistance in lake management, and development of the Oregon Aquatic Nuisance Species Management Plan.  Major funding sources include US EPA, Pacific States Marine Fisheries Commission, Oregon Watershed Enhancement Board, US Coast Guard, US Fish and Wildlife Service, and the Bonneville Power Administration. Dr. Sytsma will assist in design and implementation of all project elements and be primarily responsible for project administration at PSU.

# Stan Geiger, M.S.

Project Manager, Team Investigator

Center for Lakes and Reservoirs

Stan Geiger, wetland scientist and phycologist, has 26 years of professional and managerial experience as a consulting scientist.  His experience includes strategic planning for environmental permitting, wetland and watershed restoration, design and construction of treatment wetlands, development of natural resource management plans, development of receiving water nutrient standards, and management of multidiscipline project teams.

Mr. Geiger is a professional wetland scientist and has managed the design, construction, and monitoring of constructed wetlands and steam enhancements.  Many of these wetlands have functioned to improve the quality of storm and wastewater or have been developed as wetland and wildlife habitat as compensatory mitigation.  He has been active in the development of wetland mitigation banks for operation by both private and public sector clients.

Mr. Geiger has been involved extensively in the permitting of development projects with potential impacts on a variety of natural resource elements, including receiving waters, wetlands and threatened and endangered plant and animal species. He has been the principal investigator and project manager on projects that have entailed the collection and analysis of flow and water quality data to assess sources of nutrients to receiving waters.  He has authored restoration analyses that set direction for the restoration of wetlands, watersheds and associated streams and lakes.

He has addressed the practical problems of managing over-fertilized lakes in a variety of long-term quantitative studies of lakes in Oregon and Washington.  He has managed USEPA Clean Lake-sponsored studies of Lacamas Lake in Washington and Blue Lake and Garrison Lake in Oregon.  He has managed a public-private partnership study of Lake Oswego on the Tualatin River in Oregon for the Unified Sewerage Agency, the Lake Oswego Corporation and the Oregon Department of Environmental Quality.

Mr. Geiger's research interests and work as a consulting scientist have included the use of Geographical Information Systems for organizing and assessing lanscape data; study of plants and their interaction with aquatic environments; creation and assessment of new wetlands; control and management of nuisance wetland species, such as Eurasian water-milfoil and reed canarygrass; study of algal and aquatic macrophyte responses to eutrophication; and distribution of algae in oligotrophic and eutrophic lakes in the Northwest.

Education

Post-Graduate Studies

Portland Community College, 1998

Portland State University, 1975-1981

Oregon State University, 1973-74

M.S. Botany, Phycology, University of Missouri, 1973

M.Div. Theology, Psychology, Yale University, 1963

B.A. Philosophy, Biology, Central Methodist College, 1958

### Certifications

Society of Wetland Scientists Professional Wetland Scientist  000454

Eric Henry, Ph.D.

[Need rearranging somehow]

EDUCATION:
Institution Major [huh?]
Degree

University of British Columbia Botany Ph.D. 11/80
Oregon State University Botany M.S. 1/76
University of Connecticut Biology B.A. 6/71

Post-doctoral research fellowships from 1980 to 1988 at Harbor Branch
Oceanographic Institution, Memorial University of Newfoundland, University
of Konstanz (Germany); research focus: life histories and systematics of
marine algae

Research Associate at Oregon State University from 1988 to 1995; research
focus: viruses infecting algae

Technical and Quality Manager at PuriPonics LLC 1996- present; research
focus: physiology and mass-culture of freshwater microalgae, especially
isolates from Upper Klamath Lake.

Areas of expertise: Culture studies of algal life histories and physiology;
mass-culture of algae; algal viruses; algal systematics; light and electron
microscopy

John Rueter, Ph.D.

[need a bit more here, too modest by far]

John Rueter is a professor in the Environmental Sciences Program at PSU.
His research interests include; photosynthesis responses, trace metal
nutrition and modeling approaches for algal metabolism.  His laboratory is
equipped for photosynthetic oxygen production, pigment analysis and
fluorometric assays of reactive oxygen species.  Professor Rueter received
his Ph.D. from MIT in 1979.

## References

###### FROM GEIGER PAPER

Atkins, Glenn J.  1970.  The effects of land use and land management on the wetlands of the Upper Klamath Basin.  M.Sc. Thesis presented to Western Washington State College, Bellingham, Washington.  March 1970.

Barber, Larry B., Jerry A. Leenheer, Ted I. Noyes, and Eric A. Stiles.  1999.  Wetlands and riparian habitat initiative.  Transformation of dissolved organic carbon in constructed wetland systems.  Prepared for the Bureau of Reclamation, Denver, Co.  Prepared by the U. S. Geological Survey, National Research Program, Boulder, Colorado.  January 1999.

Basdekas, Leon.  1997.  Memorandum:  Upper Klamath Lake (UKL)/Agency Lake Mapping – 1997 Revised Area-Capacity.  Bureau of Reclamation, Klamath Basin Area Office.

Berman, T.,and S. Chava.  1999.  Algal growth on organic compounds as nitrogen sources.  Journal of Plankton Research.  8:1423-1437.

Bortleson, Gilbert C. and Marvin O. Fretwell.  1993.  A review of possible causes of nutrient enrichment and decline of endangered sucker populations in Upper Klamath Lake, Oregon.  Water Resource Investigations Report 93-4087, Portland, Oregon, U.S. Geological Survey, 1993.

Carlson, J. R.  1993.  The evaluation of wetland changes around Upper Klamath Lake, Oregon using multitemporal remote sensing techniques.  Pages 197-201 in S. Campbell, ed.  Environmental research in the Klamath Basin, Oregon.  1991 Annual Report.  U. S. Department of the Interior, Bureau of Reclamation, Denver Office.  April 1993.

Cowardin, L. M., V. Carter, F. C. Golet and E. T. LaRoe.  1979.  Classification of wetlands and deepwater habitats of the United States.  FWS/OBS-79/31.  Office of Biological Services, U. S. Fish and Wildlife Service, Washington, D.C.

DeHaan, H., H. L. Hoogveld, T DeBoer, J. Voerman, J.R. Moed.  1988.  Manipulation of chemistry and phytoplankton by hydrological intervention:  a whole lake experiment in the Northern Netherlands.  Freeshwater Biology 20:395-406.

Devol, A.H., A. Dos Santos, B.R. Forsberg, T.M. Zaret.  1984.  Nutrient addition experiments in Lago Jacarentinga, Central Amazom, Brazil:  2>  The effect of humic and fulvic acids.  Hydrobiologia.  109:97-103.

Eilers, J., J. Kann, J. Cornet, K. Moser, A.St. Amand, and C. Gubala.  2001.  Recent paleolimnology of Upper Klalath Lake, Oregon.  Prepared for the U. S. Bureau of Reclamation, Klamath Falls, Oregon.  Prepared by JC Headwaters, Inc., Roseburg, Oregon.

Forbes, Margaret.  1997.  Horizontal zonation of periphyton in Hanks Marsh, Upper Klamath Lake, Orgon.  A M.Sc. thesis presented to the faculty of Humboldt State University.  February 1997.

Forbes, Margaret G., James J. Sartoris, and David Sisneros.  1998.  Selected water quality dynamics and horizontal zonation of water quality in Hanks Marsh.  Technical Memorandum No. 8220-98-11.  Technical Service Center, Denver, Colorado.  Bureau of Reclamation.  July 24, 1998.

Gearheart, Robert.  1992.  Use of constructed wetlands to treat domestic wastewater.  City of Arcata, California.  Water Sci. Technol. 26:1625-1637.

Gearheart, Robt. A., Jeffrey K. Anderson, Margaret George Forbes, Mark Osburn, and Daniel Oros.  1995.  Watershed strategies for improving water quality in Upper Klamath Lake, Oregon - Volumes I, II and III.  Humbolt State University, August 1995.

Geiger, S., D. Caldwell and B. Hollen.  2000.  Potential water quality impacts of the Pelican Butte Ski Area Project, Klamath Falls, Oregon, including potential impacts on Upper Klamath National Wildlife Refuge Marsh.  Prepared for Cogan Owens, Cogan, Portland, Oregon.  Prepared by Shapiro and Associates, Inc., Portland, Oregon.  October 30, 2000.

Geiger, S., A. Roberts, L. Burleson, M. Warren, G. Rand, B. Lind, and W. Ormiston.  2001.  Sevenmile Canal-Wood River watershed, Klamath County, Oregon:  Evaluation of nutrient loading sources and options for water quality improvement on private and selected public lands.  Prepared for the Water for Life Foundation, Salem, Oregon.  Prepared by Shapiro and Associates, Inc., Portland, Oregon.  April 16, 2001.

Godshalk, G. L. and R. G. Wetzel.  1978.  Decomposition in the littoral zone of lakes.  Pages 131-141 in R. E. Good, D. F. Whigham, and R. L. Simpson (eds) Freshwater wetlands:  Ecological processes and management potential.  Academic Press, New York

.

Good, Ralph E., Dennis F. Whigham, and Robert L. Simpson.  1978.  Freshwater wetlands:  Ecological processes and management potential.  Academic Presss, N.Y.

Guildford, S.J., F.P. Healey, R.E. Hecky.  1987.  Depression of primary production by humic matter and suspended sediment in limnocorral experiments at Southern Indian Lake, Northern Manitoba.  Canadian Journal of Fisheries and Aquatic Sciences.  44:1407-1408.

Hammer, Donald A. (Ed.)  1989.  Constructed wetlands for wastewater treatment.  Proceedings of the First International Conference on Constructed Wetlands for wastewater Treatment, Chattanooga, Tennessee, June 13-17, 1988.  Lewis Publishers, Chelsea, Michigan.

Havens, K.E., E. J. Phlips, M. F. Cichra, and B. Li.  1998.  Light availability as a possible regulator of cyanobacteria species composition in a shallow subtropical lake.  Freshwater Biology  39:547-556.

Jackson, T.A., R.E.  Hecky.  1980.  Depression of primary productivity by humic matter in lake and reservoir waters of the boreal forest zone.  Canadian Journal of Fisheries and Aquatic Sciences.  37: 2300-2317.

Johnson, Daniel M., Richard Petersen, D. Richard Lycan, James W. Sweet, Mark E. Neuhaus, and Andrew L. Schaedel.  1985.  Atlas of Oregon lakes.  Oregon State University Press, Corvallis, Oregon.

Jones, R.I., P. J. Shaw, H. DeHaan.  1993.  Effects of dissolved humic substances on the speciation of iron and phosphate at different pH and ionic strength.  Environmental Science and Technology 27:1052-1059.

Kadlec, Robert H. and Robert L. Knight.  1996.  Treatment wetlands. CRC Lewis Publishers, Boca Raton, FLA

Kann, Jacob.  1998.  Compilation of Klamath Tribes inflow nutrient data, 1991-1998.  Prepared by J. Kann, Aquatic Ecosystem Sciences, LLC, Ashland, OR.  Prepared for the Klamath Tribes Natural Resources Department.  December 10, 1998.

Kann, J.  1999.  Compilation of Klamath Tribes Upper Klamath Lake water quality data, 1990-1999.  Aquatic Ecosystem Sciences LLC, prepared for Klamath Tribes Natural Resources Department, USBR Cooperative Studies, Electronic Excell File ULK90-99.XLS, December 1999.

Kann, J. and W. Walker.  1999.  Nutrient and hydrologic loading to Upper Klamath Lake, Oregon 1991-1998 (Draft Report).  Prepared for the Bureau of Reclamation, Klamath Falls, Oregon.

Keough, Janet R., Todd A. Thompson, Glenn R. Guntenspergen, and Douglas A. Wilcox.  1999.  Hydrogeomorphic factors and ecosystem responses in coastal wetlands of the Great Lakes.  Wetlands.  19(4):  821-834.

Kim, Bomchul and Robert G. Wetzel.  1993.  The effect of dissolved humic substances on the alkaline phosphatase and the growth of microalgae.  Verh. Internat. Verein. Limnol. 25:129-132, 229.

Klamath Consulting Service, Inc.  1983.  The Upper Klamath EPA 314 Clean Lakes Program 1981-1983 Phase I diagnostic/feasibility study.  Prepared for Klamath County, Oregon by Klamath Consulting Service, Inc., Klamath Falls, Oregon.

Laenen, Antonius and A.P. LeTourneau.  1996.  Upper Klamath Basin nutrient-loading study estimate of wind-induced resuspension of bed sediment during periods of low lake elevation.  Open-File Report 95-414, Portland, Oregon, U.S. Geological Survey, 1996.

Lodge, D. M., J. W. Barko, D. Strayer, J. M. Melack, G. G. Mittelbach, R. W. Howarth, B. Menge, and J. E. Titus.  1988.  Spatial heterogeneity and habitat interactions in lake communities.  Pages 181-208 in Stephen R. Carpenter ed. Complex interactions in lake communities.  Springer-Verlag.

Miller, William E. and Jerry C. Tash.  1967.  Interim Report, Upper Klamath Lake Studies, Oregon.  Eutrophication Research Branch, Pacific Northwest Water Laboratory, Corvallis Oregon.  Federal Water Pollution Control Administration.  September 1967.

Mitsch, William J., Alex J. Horne and Robert W. Nairn.  2000.  Nitrogen and phosphorus retention in wetlands – ecological approaches to solving excess nutrient problems.  Ecological Engineering.  14: 1-7

Moshiri, Gerald A. (ed)  1993.  Constructed wetlands for water quality improvement.  Lewis Publishers, Boca Raton, FLA.

Peek, Chester.  1963.  The humic water of Klamath Marsh and its effect on the growth of Anabaena cylindrical Lemm. In culture.  Ph.D. Thesis, Oregon State University, May 15, 1963.

Perdue, E.M., C.R. Lytle, M.S. Sweet and J.W. Sweet.  1981.  The chemical and biological impact of Klamath Marsh on the Williamson River, Oregon.  Environmental Sciences and Resources, Portland State University, Portland, Oregon.  Prepared for Water Resources Research Institute, Oregon State University.  WRRI-71.  March 1981.

Phil Williams and Associates, Inc.  2001.  Evaluation of proposed lake management on hydrodynamics, water quality and eutrophication in Upper Klamath Lake.  Prepared for the U. S. Bureau of Reclamation, Klamath Falls, Oregon.  Prepared by Phillip Williams and Associates, Inc., Portland, Oregon with Danish Hydraulic Institute-Institute of Water Environment (DHI), Philadelphia, Pennsylvania and Horsholm, Denmark.  March 28, 2001.

Phinney, Harry K., Chester A. Peek, and J. L. McLachlan.  1959.  A survey of phytoplankton problems in Klamath Lake.  Report to the Supporting Agencies.  Oregon State University, Corvallis, Oregon.

Phinney, Harry K. and Chester A. Peek.  1961.  Klamath Lake, an instance of natural enrichment.  Pages 22-27 in Algae and metropolitan wastes:   Transactions of the seminar on algae and metropolitan wastes, Robert A. Taft Sanitary Engineering Center, Cincinnati, Ohio, 1960.

Prentki, R. T., T.D. Gustafson, and M. S. Adams.  1978.  Nutient movements in lakeshore marshes.  Pages 169-194 in R. E. Good, D. F. Whigham, and R. L. Simpson (eds) Freshwater wetlands:  Ecological processes and management potential.  Academic Press, New York.

Rykbost, Kenneth.  2001.  Superintendent of Oregon State University, Agriculture Experiment Station, Klamath Falls, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon May 15, 2001.

Sartoris, J. J. and D. Sisneros.  1993.  Upper Klamath Lake wetlands study.  Pages 189-196 in S. Campbell, ed.  Environmental research in the Klamath Basin, Oregon.  1991 Annual Report.  U. S. Department of the Interior, Bureau of Reclamation, Denver Office.  April 1993.

Sartoris, J.J., D. Sisneros, and S.G. Campbell.  1993.  Upper Klamath Lake wetlands study.  Pages 189 - 221 in S. Campbell, ed.  Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  USDI, Bureau of Reclamation, Applied Sciences Branch, Research and Laboratory Services Division, Denver, CO.  September 1993.

Shapiro and Associates, Inc.  2001.  Running Y Ranch Resort, Caledonia Marsh Wetland Restoration Test Unit, Third-Year growing season monitoring report (fourth monitoring report).  Prepared for Running Y Ranch Resort, Klamath Falls, Oregon.  Prepared by Shapiro and Associates, Inc., Portland, Oregon. January 17, 2001.

Snyder, Daniel T. and Jennifer L. Morace.  1997.  Nitrogen and phosphorus loading from drained wetlands adjacent to Upper Klamath and Agency Lakes, Oregon.  U. S. Geological Survey, Water-Resources Investigations Report 97-4059.  Prepared in cooperation with the Bureau of Reclamation.  Portland, Oregon.

SRI/Shapiro, Inc. 1994.  Final 1992 report on monitoring of Jackson Bottom Experimental Wetland (JBEW; 1990-1992).  Prepared for the Unified Sewerage Agency, Hillsboro, Oregon. SRI/Shapiro, Inc., Portland, Oregon, in association with Luzier Hydrosciences, Portland, Oregon.  November 16, 1994.

U. S. Bureau of Reclamation.  2001.  Digital file of end-of-month lake elevations and Basdekas (1997 memorandum), Jim Bryant.  Personal communication with S. Geiger, Shapiro and Associates, Inc. May 15, 2001.

U. S. Environmental Protection Agency.  2000.  Constructed wetlands treatment of municipal wastewaters.  EPA/625/R-99/010  Office of Research and Development, Cincinnati, Ohio.  September 2000

Walker,W.  2001.  Development of a phosphorus TMDL for Upper Klamath Lake, Oregon.  Prepared for the Oregon Department of Environmental Quality, Bend, Oregon.  Prepared by W. Walker, Concord, Massachusetts.  March 7, 2001.

Wetzel, Robert.  1975.  Limnology.  W. B. Saunders Company, Philadelphia.

Xue, H., L. Sigg.  1999.  Comparison of the complexation of Cu and Cd by humic and fulvic acids and by ligands observed in lake waters.  Aquatic Geochemistry.  5:313-335.

FROM SHAPIRO SEVENMILE CANAL-WOOD RIVER REPORT (2001)

Albright, Jeff.  1999.  Hydrologist, National Park Service, Fort Collins, Colorado.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, December 16, 1999.

Atkins, Glen J.  1970.  The effects of land use and land management on the wetlands of the Upper Klamath Basin.  Thesis Paper presented to Western Washington State College, March 1970.

Azevedo, J., and P.R. Stout.  1974.  Farm animal manures:  An overview of their role in the agricultural environment.  California Agric. Exp. Station Extension Service.  Manual 44. Ag. Publication.  Univ. of Calif. Berkeley, Calif.  94720.

Bernton, Hal.  1997.  Worlds collide in Klamath Basin.  The Sunday Oregonian.  November 16, 1997.  Pages A1, A16, A17.

Biggs, B. J. F.  2000.  Eutrophication of streams and rivers:  Dissolved nutrient – chlorophyll relationships for benthic algae.  J.N. Am. Benthol.  Soc. 19:17-31.

Bortleson, Gilbert C. and Marvin O. Fretwell.  1993.  A review of possible causes of nutrient enrichment and decline of endangered sucker populations in Upper Klamath Lake, Oregon.  Water Resource Investigations Report 93-4087, Portland, Oregon, U.S. Geological Survey, 1993.

Brownell, Dorie L. and Mia R. Rinallo.  1995.  A selected bibliography of water related research in the Upper Klamath Basin, Oregon.  Open-File Report 95-285, Portland, Oregon, U.S. Geological Survey, 1995.

Campbell, Sharon, ed.  1993a.  Environmental research in the Klamath Basin, Oregon.  1991 Annual Report.  R-93-13.  USDI, Bureau of Reclamation, Applied Sciences Branch, Research and Laboratory Services Division, Denver, CO.  April, 1993.

Campbell, Sharon, ed.  1993b.  Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  USDI, Bureau of Reclamation, Applied Sciences Branch, Research and Laboratory Services Division, Denver, CO.  September 1993.

Campbell, Sharon.  1999.  Flow and water quality data, Wood River Basin, 1991-1993.  Collected by Bureau of Reclamation, Denver, Colorado.  Personal communication.

Campbell, Sharon.  2000.  Sevenmile Canal flow direction.  Personal communication, January 18, 2000.

Chetelat, J., F.R. Pick, and A. Moran.  1999.  Periphyton biomass and community composition in rivers of different nutrient status.  Can. J. Fish Aquat.  Sci. 56(4):560-569.

Cheyne, Steve.  1999.  Irrigation Scheduling Technician, Oregon State University Extension Service, Klamath Falls, Oregon.  Personal communication with Stan Geiger, SHAPIRO, October 19, 1999.

Cowardin, Lewis M., V. Carter, F.C. Golet, and E.T. LaRoe.  1979.  Classification of wetlands and deepwater habitats of the United States.  FWS/OBS-79/31, December 1979.  Prepared for the Office of Biological Services, Fish and Wildlife Service, U.S. Department of Interior, Washington, D.C.

Department of the Interior.  50 CFR part 17.  Endangered and threatened species:  Lost River Sucker, etc. proposed rule.  Fish and Wildlife Service.  Federal Register Thursday December 1, 1994, pp. 61744-61759.

Dodds, W.K., J.R. Jones, and E.B. Welch.  1998.  Suggested classification of stream trophic state:  Distributions of temperature stream types by chlorophyll, total nitrogen, and phosphorus.  Water Res.  32:1455-1462.

Dodds, W.K., V.H. Smith, and B. Zander.  1997.  Developing nutrient targets to control benthic chlorophyll levels in streams:  A case study of the Clark Fork River.  Water Res.  31:1738-1750.

Ehinger, W.J.  1993a.  Wood River nutrient export study.  Pages 15-21 in S. Campbell, ed. Environmental Research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  USDI, Bureau of Reclamation. Denver Office.

Ehinger, W. J.  1993b.  Experimental studies of trophic relationships among nutrients, phytoplankton, zooplankton, and fish.  Pages 81-102 in S. Campbell, ed. Environmental Research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-13.  USDI, Bureau of Reclamation. Denver Office.

Ehinger, W. J.  1993c.  Results of experimental studies of the effects of nutrients and zooplankton on blue-green algae in Agency Lake.  Pages 139-188 in S. Campbell, ed. Environmental Research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  USDI, Bureau of Reclamation. Denver Office.

Ehinger, W. J.  1992.????  Experimental studies of the effects of nutrients and Daphnia grazing on phytoplankton biomass and growth in a hypertrophic lake (Agency Lake, Oregon).  Dissertation.  University of North Carolina at Chapel  Hill.

Environmental Laboratory, 1987.  Corps of Engineers Wetlands Delineation Manual, Technical Report Y-87-1, US Army Engineer Waterways Experimental Station, Vicksburg, Miss.

Frankenbach, Rolf I. and  Joseph S. Meyer.  1999.  Nitrogen removal in a  surface-flow wastewater treatment wetland.  Wetlands Volume 19(2):403-412.

Fregien, Susan.  1999.  Characterization of moist-soil plant communities within seasonal wetlands created by flooding agricultural fields on the Tule Lake NWR.  Paper presented at the Third Klamath Basin Watershed Restoration and Research Conference.  March 9-11, 1999, Klamath Falls, OR.

Garlock, Devan.  1999.  Manager, Oregon Department Fish Hatchery, Crooked Creek, Chiloquin, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon October 22, 1999.

Gearheart, Robt. A., Jeffrey K. Anderson, Margaret George Forbes, Mark Osburn, and Daniel Oros.  1995a.  Watershed strategies for improving water quality in Upper Klamath Lake, Oregon - Volume I.  Humbolt State University, August 1995.

Gearheart, Robt. A., Jeffrey K. Anderson, Margaret George Forbes, Mark Osburn, and Daniel Oros.  1995b.  Watershed strategies for improving water quality in Upper Klamath Lake, Oregon - Volume II.  Humbolt State University, August 1995.

Gearheart, Robt. A., Jeffrey K. Anderson, Margaret George Forbes, Mark Osburn, and Daniel Oros.  1995c.  Watershed strategies for improving water quality in Upper Klamath Lake, Oregon - VolumeIII.  Humbolt State University, August 1995.

Hart, J., M. Gangwer, M. Graham, and E. S. Marx.  ~1997. Nutrient management for dairy production:  Dairy manure as a fertilizer source. EM8586.  Oregon State University Extension Service.

Hatfield, J. L. and B. A. Stewart. Eds. 1997.  Animal waste utilization.  Effective use of manure as a soil resource.  CRC press, Boca Raton, FLA.

Hathaway, Ronald L.  1999.  Oregon State University Extension Service, Klamath Falls, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., September 30, 1999.

Hathaway, Ronald L. and Rodney Todd.  1993.  Wood River sub-basin water quality as related to land use associated with forest and livestock grazing.  Final Technical Completion Report.  Submitted to the U. S. Department of the Interior, Geological Survey, Reston, Virginia.  Project sponsored by the Oregon Water Resources Research Institute, Oregon State University, Corvallis, OR.  Prepared by the Oregon State University Extension Service, Klamath County Office.  November 1993.

Hawkins, Gerald.  1999.  Manager, Meadows Drainage District, Fort Klamath, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, September 16, 1999.

Hubbard, Larry L.  1970.  Water budget of Upper Klamath Lake Southwestern Oregon.  Hydrologic Investigations Atlas HA-351.  Prepared in cooperation with the U. S. Public Health Service.  Published by the U. S. Geological Survey, Washington, D. C.

Illian, Joseph R.  1970.  Interim report on the ground water in the Klamath Basin, Oregon.  Issued by Chris L. Wheeler, State Engineer, Salem, Oregon.  November 1970.

Johnson, Daniel M., Richard Petersen, D. Richard Lycan, James W. Sweet, Mark E. Neuhaus, and Andrew L. Schaedel.  1985.  Atlas of Oregon lakes.  Oregon State University Press, Corvallis, Oregon.

Kadlec, R.H. and R.L. Knight.  1996.  Treatment Wetlands.  CRC/Lewis Publishing, Boca Raton, Florida.

Kann, Jacob.  1993a.  Agency Lake limnology, 1990-1991 – USBR – Klamath Tribes cooperative studies.  Pages 103-110 in S. Campbell ed. Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-13.  April 1993.  U. S. Department of the Interior, Bureau of Reclamation, Denver Office.

Kann, Jacob. 1993b.  Agency Lake limnology 1992.  Pages 91-97 in S. Campbell, ed. Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  September 1993.  U. S. Department of the Interior, Bureau of Reclamation, Denver Office.

Kann, Jacob.  1993c.  Description of methods used to predict Wood River discharge at Weed Road and Dike Road.  Pages 12-15 in S. Campbell ed., Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  September 1993.  U. S. Department of the Interior, Bureau of Reclamation, Denver Office.

Kann, Jacob.  1997.  Ecology and water quality dynamics of a shallow hypereutrophic lake dominated by cyanobacteria.  PhD Dissertation, U. of North Carolina at Chapel Hill.

Kann, Jacob.  1998.  Compilation of Klamath Tribes inflow nutrient data, 1991-1998.  Prepared by J. Kann, Aquatic Ecosystem Sciences, LLC, Ashland, OR.  Prepared for the Klamath Tribes Natural Resources Department.  December 10, 1998.

Kann, Jacob.  1999.  Principal, Aquatic Ecosystem Sciences, LLC, Ashland, OR.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, November 19, 1999.

Keith, Diane.  1999.  Klamath County Soil and Water Conservation District project manager.  Personal communication with R. Craven and S. Geiger, Shapiro and Associates, Inc., August 1999.

Kepple, Todd.  1998a.  Wetland conversion impact focus of latest federal report.  Herald and News, Klamath Falls, Oregon.  January 11, 1998.  Pages 1, 2.

Kepple, Todd.  1998b.  Special Report:  Upper Klamath Lake.  Herald and News, Klamath Falls, Oregon.  January 11, 1998, Pages 1B-8B.

Kirk, Steve.  1999.  Senior Water Quality Specialist, Eastern Region, Oregon Department of Environmental Quality, Bend, Oregon.  Personal Communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, October 27, 1999.

Klamath Consulting Service, Inc.  1983.  The Upper Klamath EPA 314 Clean Lakes Program 1981-1983 Phase I diagnostic/feasibility study.  Prepared for Klamath County, Oregon by Klamath Consulting Service, Inc., Klamath Falls, Oregon.

Laenen, Antonius and A.P. LeTourneau.  1996.  Upper Klamath Basin nutrient-loading study estimate of wind-induced resuspension of bed sediment during periods of low lake elevation.  Open-File Report 95-414, Portland, Oregon, U.S. Geological Survey, 1996.

Lytle, Charles R. and Edward M. Perdue.  1981.  Free, proteinaceous, and humic-bound amino acids in river water containing high concentrations of aquatic humus.  Environmental Science & Technology 15(2):222-228.

McAuliff, Ambrose.  1999.  Rancher, Wood River Valley, Fort Klamath, Oregon.  Personal communication with R. Craven, Shapiro and Associates, Inc., Portland, Oregon, August 11, 1999.

Miller, William E. and Jerry C. Tash.  1967.  Interim Report, Upper Klamath Lake Studies, Oregon.  Eutrophication Research Branch, Pacific Northwest Water Laboratory, Corvallis Oregon.  Federal Water Pollution Control Administration.  September 1967.

Moon, David C.  1997.  “Klamath adjudication” in Flexibility in Oregon water law:  the sixth annual Oregon water law conference.  Oregon Insider.  Issue #188, November 15, 1997.

Moore, James A. and Michael J. Gamroth.  ~1993.  Calculating the fertilizer value of manure from livestock operations. EC 1094.  Oregon State University Extension Service.

Moshiri, Gerald A. ed.  1993.  Constructed wetlands for water quality improvement.  CRC Press, Boca Raton, Florida.

Nader, Glenn, Kenneth W. Tate, Robert Atwill, and James Bushnell.  1998.  Water quality effect of rangeland beef cattle excrement.  Rangelands 20(5):19-25.

Nicholson, Roger.  2000.  Rancher, Wood River Valley, Fort Klamath, Oregon.  Personal communication with R. Craven, Shapiro and Associates, Inc.  Portland, Oregon, February 11, 2000.

Nordin, R.N.  1985.  Water Quality Criteria for Nutrients and Algae (Technical Appendix).  British Columbia Ministry of the Environment, Victoria, BC.  104 pp.

Norman, Russell, Louise Finger, Doug Titus, and Robert Gearhart.  1993.  Review of wetland evapotranspiration literature.  Prepared for the Bureau of Reclamation, Klamath Falls, Oregon, by Humbolt State University, May 1993. Prepared by Environmental Resources Engineering Department, Humbolt State University, Arcata, California.

Northwest Biological Consulting.  1997.  Agency Lake Ranch constructed wetland project.  Klamath County, Oregon.  Feasibility and cost estimate.  Submitted to Water for Life Foundation, Salem, Oregon.  June 30, 1997.

OAR (Oregon Administrative Rules).  2000.  Water Quality Program Rules, 340-041-0150, Nuisance Phytoplankton Growth.

OECD.  1982.  Eutrophication of Waters: Monitoring, Assessment and Control.  OECD, Paris.  154 pp.

Oregon Department of Environmental Quality et al.  1999.  Water quality monitoring technical guide book.  Complement to the GWEB Watershed Assessment Manual and the Oregon Plan for Salmon and Watersheds.  Prepared by Interagency Water Quality Monitoring Team.  July 1999.

Oregon Department of Environmental Quality.  1998.  DEQ Laboratory quality assurance manual.  ODEQ, Laboratory Division, 1712 SW. 11th Avenue, Portland, Oregon  97201.  July 1998.

Oregon Department of Fish and Wildlife.  May, 1994.  Aquatic Inventories Project:

Stream Survey Methods.  Version 4.0.  Oregon Department of Fish and Wildlife, Research and Development Section, Corvallis, Oregon.

Oregon Department of Fish and Wildlife.  November, 1996.  Klamath River Basin,

Oregon Fish Management Plan-Draft.  Oregon Department of Fish and Wildlife, Klamath District Office, Klamath Falls, Oregon.

Oregon Water Resources Department.  1999.  Klamath basin adjudication.  Digital document on the WRD state web site www.wrd.state.or.us/programs/klamath/summary

Comprised of 15 document sections.

Oregon Department of Fish and Wildlife.  1999.  Personal communication, Devan Garlock, Manager 2, Klamath Fish Hatchery, Fort Klamath, Oregon.  Quarterly Discharge Monitoring Reports (Permit No. 0300-J; Discharge No. OR 002765-1), March, May and September 1998.

Peek, C.A.  1963.  The humic water of Klamath Marsh and its effect on the growth of Anabaena cylindrica Lemm. in culture.  Oregon State University, Ph.D. dissertation.

Peek, C.A. and Phinney, H.K.  1962.  Investigation into methods to control algae in the Klamath River Basin:  Klamath Falls, Oregon.  Klamath River Compact Commission.

Perdue, E.M., C. R. Lytle, M. S. Sweet, and J. W. Sweet.  1981.  The chemical and biological impact of Klamath Marsh on the Williamson River, Oregon.  Environmental Sciences and Resources, Portland State University, Portland, Oregon, March 1981.

Petersen, R.G., H.L. Lucas, and W.W. Woodhouse, Jr.  1956.  The distribution of excreta by freely gazing cattle and its effect on pasture fertility.  I.  Excretal distribution.  Agron. J.  48:440-444.

Phillips, W.A.  1998.  Use of manure on grazing lands.  Pages 157-171 in J.L. Hatfield and B.A. Stewart, eds.  Animal waste utilization:  effective use of manure as a soil resource.  Ann Arbor Press, Michigan.

Porcella, Donald B., Spencer A. Peterson, and David P. Larsen.  Index to evaluate lake restoration.  Journal of the Environmental Engineering Division.  EE6 (15893):1151-1169.

Quinn, J.M.  1991.  Guidelines for the Control of Undesirable Biological Growths in Water.  National Inst. Water and Atmos. Res., Consultancy Report No. 6213/2.

Redmond, Kelly T.  1990.  Crater Lake climate and lake level variability.  Pages 127-141 in E. T. Drake, G. L. Larson, J. Dymond and R. Collier, eds. Crater Lake:  An ecosystem study.   Papers presented at the sixty-ninth annual meeting of the Pacific Division of the American Association for the Advancement of Science, Oregon State University, Corvallis, Oregon, June 18-22, 1988.

Reed, Sherwood, Ronald Crites, and Joe Middlebrooks.  1995.  Natural systems for waste management and treatment.  Second edition.  McGraw-Hill, New York.

Renne, Dan.  1999.  Steward of The Nature Conservancy Tulana Farms project, Upper Klamath Lake, and past foreman of the L. Garrison Tulana Farms Agency Lake Ranch 1992-1998.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, December 7, 1999.

Richardson, Patricia Q. and R.H. Richardson.  2000.  Dung beetles improve the soil community (Note).  Ecological Restoration 18(2):116.

Risley,  John C. and Antonius Laenen.  1999.  Upper Klamath Lake Basin nutrient-loading study-asessment of historic flows in the Williamson and Sprague Rivers.  U. S. Geological Survey Water-Resource Investigations Report 98-4198.  Prepared in cooperation with Bureau of Reclamation.  Portland, Oregon.

Rykbost, K. A.  1999.  Superintendent/Professor Klamath Experiment Station, Klamath Falls, OR.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, OR, August 19, 1999.

Rykbost, K. A., B. A. Charlton and R. L. Dovel.  1999.  Nutrient loading in Klamath/Agency Lakes and background sources.  Report from Klamath Experiment Station, Klamath Falls, Oregon.  March 1999.

Sartoris, J.J., D. Sisneros, and S.G. Campbell.  1993.  Upper Klamath Lake wetlands study.  Pages 189 - 221 in S. Campbell, ed.  Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  USDI, Bureau of Reclamation, Applied Sciences Branch, Research and Laboratory Services Division, Denver, CO.  September 1993.

Shapiro and Associates, Inc. 1999.  [Monitoring report Running Y for second year of Test Unit operation].

Shapiro and Associates, Inc.  1999.  Watershed restoration project proposal for construction and testing of pilot water quality treatment facilities and development of hydrology and water quality databases or Sevenmile Canal and Wood River.  Prepared by Shapiro and Associates, Inc., Portland, Oregon for the Water for Life Foundation, Salem, Oregon and the Bureau of Reclamation, Klamath Falls, Oregon January 8, 1999.

Shapiro and Associates, Inc. 2000.  RunningY Ranch Resort third-year report, second-year monitoring report.  Prepared for RunningY Ranch Resort, Klamath Falls, Oregon.  Prepared by Shapiro and Associates, Inc., Portland, Oregon.  February 24, 2000.

Smith, Roger.  1999.  Letter of April 10, 2000 to Curt Mullis, USFWS Klamath Falls.  Letter contained review comments on Draft Shapiro Wood River report.

Smith, R. Daniel, Alan Ammann, Cindy Bartoldus, and Marla M. Brinson.  1995.  An approach for assessing wetland functions using hydrogeomorphic classification, reference wetlands, and functional indices.  USACE Wetlands Research Program Technical Report WRP-DE-9.

Snyder, Daniel T.  1999.  Project Manager, lead scientist, U. S. Geological Survey, Portland, Oregon.  Personal Communication with S. Geiger, Shapiro and Associates, Inc., Portland, OR, July 26 and October 21, 1999.

Snyder, Daniel T. and Jennifer L. Morace.  1997.  Nitrogen and phosphorus loading from drained wetlands adjacent to Upper Klamath and Agency Lakes, Oregon.  U. S. Geological Survey, Water-Resources Investigations Report 97-4059.  Prepared in cooperation with the Bureau of Reclamation.  Portland, Oregon.

Sosiak, A.J.  Personal Communication.  Long-term response of periphyton and macrophytes to reduced municipal nutrient loading to the Bow River (Alberta, Canada).  Alberta Environmental Protection, Calgary, Alberta.

Sparks, Dell.  1999.  Watermaster, Klamath Basin, Oregon, Oregon Deparment of Water Resources, Klamath Falls.  Personal communication May 19, 1999.

Stayer, Bob.  1999.  Lewis Matthis Ranch Foreman, Fort Klamath, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, September 2, 1999.

Stroud, Bill.  1999.  Laboratory Manager, Pacific Northwest Regional Laboratories, U. S. Bureau of Reclamation, Boise, Idaho.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, December 8, 1999.

Thomas,E. K., and R. Ford.  1993.  Fishes of United States Forest Service Streams

Within the Klamath Basin, Oregon-Draft.  USDA Forest Service, Pacific Northwest Region, Winema National Forest, 2819 Dahlia Street, Klamath Falls, Oregon.

UK Environment Agency.  1998.  Aquatic Eutrophican in England and Whales.  Environmental Issues Series Consultative Report.

U.S. Army Corps of Engineers.  1982.  Potential eutrophication control measures for Upper Klamath Lake, Oregon:  Data evaluation and experimental design.  Klamath River Basin Water Resources Development Project Contract No. DACW07-81-C-0045.  USACE, San Francisco District, October 1982.

U.S. Bureau of Land Management.  1995. 1995 monitoring report.  Wood River Wetland Plan Baseline Surveys.  BLM-Klamath Falls Resource Area (KFRA).  BLM, Klamath Falls, Oregon.

U.S. Bureau of Land Management.  1997.  Wood River wetland 1997 monitoring report.  BLM-Klamath Falls Resource Area (KFRA).  BLM, Klamath Falls, Oregon.

U.S.D.A., Soil Conservation Service.  1977.  Soil survey of Klamath County, Oregon, Southern Part.  Supervised by Joe Calhoon, SCS.  Prepared by SCS in cooperation with the Oregon Agricultural Experiment Station.

U. S. Environmental Protection Agency.  1975.  National Eutrophication Survey methods, 1973-1976.  Working Paper No. 175.  Pacific Northwest Environmental Research Laboratory. Corvallis, Oregon.  June 1975.

Vaga, Ralph.  2000.  Regional Nutrient Coordinator Region 10, U.S. Environmental Protection Agency, Seattle, Washington.  Information on standards available at http://www.epa.gov/ost/criteria/nutriet/guidance/.  Personal communication with S. Geiger, Shapiro and Associates, Inc., August 28, 2000.

Van Nieuwenhuyse, E.E. and J.R. Jones.  1996.  Phosphorus-chlorophyll relationship in temperature streams and its variation with stream catchment area.  Can. J. Fish. Aquat. Sci. 53:99-105.

Vogel, Dave.  1997.  Measurements of total phosphorus and water temperatures in various springs, rivers, streams, and canals in the Wood River Valley, Oregon.  Prepared for The Fort Klamath Water Users Association, Fort Klamath, Oregon.  Prepared by Natural Resource Scientists, Inc., Red Bluff, California.

Walker, William W.  1995.  A nutrient-balance model for Agency Lake, Oregon.  Prepared for U. S. Department of Interior, Bureau of Reclamation, Denver, Colorado.  Prepared by W. W. Walker, Concord, Massachusetts, April 1995.

Watkins, Wedge.  1999.  Manager of Wood River Ranch, Bureau of Land Management, Klamath Falls, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon,  November 2 and 5, 1999.

Welch, E.B., R.R. Horner, and C.R. Patmont.  1989.  Prediction of nuisance periphytic biomass:  A management approach.  Water Res. 23:401-405

Welch, E.B., J.M. Jacoby, and C.W. May.  1998.  Stream quality.  In: River Ecology and Management:  Lessons form the Pacific Coastal Ecoregion.  Naiman, R.J. and R.E. Bilby (eds.).  Springer-Verlag.  Pp. 69-94.

Wildung, R. E. and R. L. Schmidt.  1973.  Phosphorus release from lake sediments.  EPA-R3-73-024.  Ecological Research Series.  Office of Research and Monitoring, U.S. Environmental Protection Agency, Washington, D.C.

Williams, John.  1999.  U. S. Geological Survey, Portland, Oregon project manager of the Williamson River loading assesment.  Personal communications with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon December 2, 3 and 8, 1999.

Wood, Tamara M, Gregory J. Fuhrer, and Jennifer L. Morace. 1996.  Relation between selected water-quality variables and lake level in Upper Klamath and Agency Lakes, Oregon.  Water-Resource Investigations Report 96-4079, Portland, Oregon, U.S. Geologic Survey in cooperation with the Bureau of Reclamation, 1996.

Wood, Wendell.  Klamath River basin:  riches at risk.  1997.  Oregon Natural Resources Council publication Wild Oregon, July 1997.

Wood, Wendell.  Wildlife:  second-class citizens on Klamath refuges.  1997.  Oregon Natural Resources Council publication Wild Oregon, July 1997.

Temperature and Precipitation Data, Chiloquin, Oregon, Oregon Climate Service, Corvallis, Oregon.

Streamflow Data, 1992 – 1997, Annie Creek Station # 61420301, U. S. Forest Service.  Obtained from the Oregon Water Resources Department web site July 21, 1999.

Streamflow Data, 1992 – 1997, Sevenmile Creek Station # 61420303, U. S. Forest Service.  Obtained from the Oregon Water Resources Department web site July 21, 1999.

Flow and Water Quality Data, STORET, Date of Results from Oregon Department of Environmental Quality Query, December 14, 1998.

Flow and Water Quality Data, 1991-1993, Wood River Watershed, Bureau of Reclamation, Denver, Colorado.  Provided by Sharon Campbell, Bureau of Reclamation Project Manager for data collection.

Measurements of total phosphorus and water temperatures in various springs, rivers, streams, and canals in the Wood River Valley, Oregon 1995 – 1996.  Prepared by Natural Resources Scientists, Inc., Red Bluff, California for The Fort Klamath Water Users Association.  March 1997.

Flow and Water Quality Data from Wood River Watershed Stations from Compilation of Klamath Tribes Inflow Nutrient Data, 1991-1998.  Prepared by Jacob Kann, Aquatic Ecosystem Sciences, Ashland, OR for Klamath Tribes Natural Resources Department.  December 10, 1998.

Watershed Restoration Project Proposal for Construction and Testing of Pilot Water Quality Treatment Facilities and Development of Hydrology and Water Quality Databases for Sevenmile Canal and Wood River.  Prepared by Shapiro and Associates, Inc., Portland, Oregon and submitted to the U. S. Fish and Wildlife Service Ecosystem Restoration Office, Klamath Falls, Oregon, on behalf of the Water for Life Foundation, Klamath Falls, Oregon.

FROM SHAPIRO PELICAN BUTTE UKLNWR ASSESSMENT (2000)

Buettner, Mark.  2000.  Project manager and fishery scientist, Bureau of Reclamation, Klamath Falls, Oregon.  Personal communication April 18, 2000 with Stan Geiger, Shapiro and Associates, Inc., Portland, Oregon.

Campbell, S. G. Ed.  1993.  Environmental research in the Klamath Basin, Oregon.  1992 Annual Report.  R-93-16.  Bureau of Reclamation, Applied Sciences Branch, Denver Office, Denver, Colorado.  September 1993.

Carlson, J. R.  1993.  The evaluation of wetland changes around Upper Klamath Lake, Oregon using multitemporal remote sensing techniques.  Pages 197-202 in S. Campbell, ed.  Environmental research in the Klamath Basin, Oregon.  1991 Annual Report.  USDI, Bureau of Reclamation, Denver Office.  R-93-13.  April 1993.

Cogan, Owens, Cogan.  2000.  Estimates of induced development effects in Upper Klamath Basin associated with the proposed Pelican Butte ski area project.  Portland, Oregon.

Cook, Bud.  2000.  Chief Engineer, Bureau of Reclamation, Klamath Falls, Oregon.  Personal communication with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon, March, 2000.

Cooper, P.F.  1993.  The use of reed bed systems to treat domestic sewage:  The European design and operations guidelines for reed bed treatment systems.  Pages 203-217 in G.A. Moshiri, ed.  Constructed wetlands for water quality improvement.  Boca Raton:  Lewis Publishers.

Eilers, J. M., T. J. Sullivan and K. C. Hurley.  1990.  The most dilute lake in the world?  Hydrobiologia 199:1-6

Eilers, J. M., J. A. Bernert, S.S. Dixit, C.P. Gubala, and P. R. Sweets.  1996.  Processes influencing water quality in a subalpine Cascade mountain lake.  Northwest Science.  Vol 70, Special Issue No. 2:  59-70.

Emcon.  1997.  Groundwater hydrology analysis for proposed Pelican Butte Ski Area environmental impact statement (maps and appendices included).

Forbes, Margaret.  1997.  Horizontal zonation of periphyton in Hanks Marsh, Upper Klamath Lake, Oregon.  MS thesis presented to the faculty of Humboldt State University, Environmental Systems:  Engineering, Arcata, California.  February 1997.

Gilbert, Richard O.  1987.  Statistical methods for environmental pollution monitoring.  Van Nostrand Reinhold, New York.

Harding Larson Associates.  2000.  Pelican Butte Ski Area Environmental Impact Statement final air quality and noise analysis.  Prepared for Winema National Forest, Klamath Ranger District, Klamath Falls, Oregon.  Prepared by Harding Lawson Associates, 707 Seventeenth Street, Denver, CO.  June 26, 2000.

Hubbard, Larry L.  1970.  Water budget of Upper Klamath Lake, Southwestern Oregon.  Hydrologic Investigations Atlas HA-351.  Prepared in cooperation with the U.S. Public Health Service.  Published by the U.S. Geological Survey, Washington, D.C.

Juza, Bo.  2000.  Evaluation of proposed lake management on hydrodynamic, water quality and eutrophications in Upper Klamath Lake using an integrated computer modeling approach.  Project briefing by Phil Williams Associates, San Francisco, California for Bureau of Reclamation, Klamath Falls, Oregon, April 11, 2000.

Kadlec, Robert and Robert Knight.  1996.  Treatment wetlands.  CRC Lewis Publishers, Boca Raton, FL.

Kann, J.  1998.  Compilation of Klamath Tribes inflow nutrient data, 1991-1998.  Prepared by J. Kann, Aquatic Ecosystem Sciences, LLC., Ashland, Oregon.  Prepared for Klamath Tribes Natural Resources Department.  December 10, 1998.

Kann, J. and W. Walker.  1999.  Nutrient and hydrologic loading to Upper Klamath Lake, Oregon, 1991-1998.  Prepared for the Bureau of Reclamation and the Klamath Tribes.

Klamath Tribe Natural Resources Department.  1991.  Klamath Tribe laboratory and field quality assurance/quality control plan.  Klamath Tribe Natural Resources Department, Chiloquin, Oregon.  April 9, 1991.

Lowe, Rex and Yangdong Pan.  1996.  Benthic algal communities as biological monitors.  Pages 705-739 in R. Jan Stevenson, Max L. Bothwell and Rex L. Lowe, eds. Algal ecology:  Freshwater benthic ecosystems.  Academic Press, San Diego.

McCormick, Paul V. and R. Jan Stevenson.  1998.  Periphyton as a tool for ecological assessment and management in the Florida Everglades.  J. Phycol. 34:  726-733.

Miranda, Ed. Jr.  2000.  Personal communication February 19, 2000 with S. Geiger, Shapiro and Associates, Inc., Portland, Oregon.  Ed Miranda, Jr., Fishing and Hunting Guide, Rocky Point, OR.

Mitsch, W.J. and J.G. Gosselink.  1993.  Wetlands. New York:  Van Nostrand Reinhold.

Moshiri, Gerald A.  1993.  Constructed wetlands for water quality improvement.  Lewis Publishers, Boca Raton, FL.

Murdoch, A. and J. A. Capobianco.  1979.  Effects of treated effluent on a natural marsh.  Journal of the Water Pollution Control Federation.  51:2243-2256.

Newton, David J. Associates, Inc.  2000.  Hydrogeologic characterization for the proposed Pelican Butte ski area, Klamath County, Oregon.  Draft.  Prepared for Cogan Owens Cogan, Portland, OR.  May 15, 2000.

Oregon Department of Environmental Quality.  1996.  1994/1996 303(d) List Of Water Quality Limited Waterbodies & Oregon's Criteria Used For Listing Waterbodies.  Issued July 1996.

Pelican Butte Corporation, 1996.  Proposed Master Development Plan for the Pelican Butte Ski Area.

Reed, Sherwood C., Ronald W. Crites and E. Joe Middlebrooks.  1995.  Natural systems for waste management and treatment.  Second edition.  McGraw-Hill Inc., New York.  433 p.

Sartoris, J. J. and D. Sisneros.  1993.  Upper Klamath Lake wetlands study.  Pages 189-197 in S. Campbell, ed. Environmental research in the Klamath Basin, Oregon.  1991 Annual Report.  USDI, Bureau of Reclamation, Denver Office, Research and Laboratory Services Division, Applied Sciences Branch.  Bureau of Reclamation Report R-93-13.  April, 1993.

Sartoris, J.J., D. Sisneros and S. G. Campbell, 1993.  Upper Klamath Lake Wetlands Study.  Pages 189-221 in S.G. Campbell, editor.  Environmental Research in the Klamath Basin, Oregon - 1991 Annual Report. USDI, Bureau of Reclamation, Denver Office, Research and Laboratory Services Division, Applied Sciences Branch.  Bureau of Reclamation Report R-93-13.

Shapiro and Associates, Inc., 1997a.  Pelican Butte Watershed Analysis.  Portland, Oregon.

Shapiro and Associates, Inc., 1997b.  Proper Functioning Condition Field Survey - Recreation Creek.

Shapiro and Associates, Inc., 1997c.  Special Status Plant Field Survey – Pelican Butte.

Shapiro and Associates, Inc.  2000a.  Project quality assurance plan.  Baseline water quality monitoring for proposed Pelican Butte Ski Resort, Klamath Falls, Oregon.  Prepared for Oregon Department of Environmental Quality, Bend, Oregon.  Prepared by Shapiro & Associates, Inc., Portland, Oregon.  February 3, 2000.

Shapiro and Associates, Inc.  2000b.  Sevenmile Canal-Wood River watershed, Klamath County, Oregon evaluation of nutrient loading sources and options for water quality improvement on private and selected public lands.  Prepared by Shapiro & Associates, Inc., Portland, Oregon.  Prepared for Water for Life Foundation, Salem, Oregon and the U. S. Fish and Wildlife Service, Klamath Falls, Oregon.  February 23, 2000.

Snyder, Daniel T.  1999.  Project Manager, lead scientist, U. S. Geological Survey, Portland, Oregon.  Personal Communication with S. Geiger, Shapiro and Associates, Inc., Portland, OR, July 26 and October 21, 1999.

Snyder, Daniel T. and Jennifer L. Morace.  1997.  Nitrogen and phosphorus loading from drained wetlands adjacent to Upper Klamath and Agency Lakes, Oregon.  U. S. Geological Survey, Water Resource Investigations Report 97-4059.

Taft, Clarence E. and W. Jack Kishler.  1973.  Cladophora as related to pollution and eutrophication in western Lake Erie.  Project Completion Report No. 332X, 339X.  U. S. Department of the Interior, State of Ohio Water Resources Center, Ohio State University.

U.S.D.A., Soil Conservation Service.  1977.  Soil survey of Klamath County, Oregon, Southern Part.  Supervised by Joe Calhoon, SCS.  Prepared by SCS in cooperation with the Oregon Agricultural Experiment Station.

USDA, 1994a.  Watershed Analysis Report for the Rock, Cherry, and Nannie Watershed Area.  USDA Forest Service, Klamath Ranger District, Winema National Forest.

USDA, 1995.  Environmental Assessment for the Nannie/Rock Planing Area.  U.S. Forest Service, Winema National Forest, Klamath Ranger District, Oregon.

USDA, 1996. North Fourmile Watershed Analysis.  USDA Forest Service, Klamath Ranger District, Winema National Forest.

U. S. Environmental Protection Agency.  1999.  Preliminary data summary of urban storm water – best management practices.  EPA-821-R-99-012.

USFWS, 1993.  Recovery Plan for the Lost River and Shortnose Sucker.  USDI Fish and Wildlife Service.  Portland, Oregon.

USFWS, 1994a.  National Wetlands Inventory Maps (Crystal Springs and Pelican Butte, 1:24000, 1984, CIR aerial photography, overlaid on 7.5-minute USGS quadrangles).

USFWS, 1994b.  Lost River and Shortnose Sucker Proposed Critical Habitat Biological Support Document-Draft.  USDI Fish and Wildlife Service.  Portland, Oregon.

USGS, 1993.  A Review of Possible Causes of Nutrient Enrichment and Decline of Endangered Sucker Populations in Upper Klamath Lake, Oregon.  Water Resources Investigations Report 93-4087.

Vymazal, Jan.  1995.  Algae and element cycling in wetlands.  Lewis Publishers, Boca Raton, Florida.  688 pp.

Wagner, D. H., 1997.  Inventory of Bryophytes and Lichens of Cherry Creek Basin Research Natural Area, Klamath County, Oregon.  Commissioned by the Winema National Forest, Oregon.  49 pp.

Walker, William W.  1995.  A nutrient-balance model for Agency Lake, Oregon.  Prepared for U. S. Department of Interior, Bureau of Reclamation, Denver, Colorado.  Prepared by W. W. Walker, Concord, Massachusetts, April 1995.

Wert and Associates, Inc.  2000a.  Pelican Butte Project.  Groundwater levels in proposed drainfield.  Report prepared for Cogan Owens Cogan, Portland, Oregon, April 25, 2000.  Prepared by Wert and Associates, Inc., Bend, Oregon.

Wert and Associates, Inc.  2000b.  Pelican Butte Project.  On-site wastewater treatment.  Report prepared for Cogan Owens Cogan, Portland, Oregon, April 25, 2000.  Prepared by Wert and Associates, Inc., Bend, Oregon.

Wert and Associates, Inc.  2000c.  Pelican Butte Project.  Run-off analysis.  Report prepared for Cogan Owens Cogan, Portland, Oregon, April 25, 2000.  Prepared by Wert and Associates, Inc., Bend, Oregon.

Wisseman, R.W., 1997.  Aquatic Invertebrate Survey of Pelican Butte in the Vicinity of the Proposed Pelican Butte Ski Area, July 22-23.  Aquatic Biology Associates, Inc., Corvallis, Oregon.

Snyder, Daniel T. and Jennifer L. Morace.  1997.  Nitrogen and phosphorus loading from drained wetlands adjacent to Upper Klamath and Agency Lakes, Oregon.  U. S. Geological Survey, Water-Resources Investigations Report 97-4059.  Prepared in cooperation with the Bureau of Reclamation.  Portland, Oregon.

SRI/Shapiro, Inc. 1994.  Final 1992 report on monitoring of Jackson Bottom Experimental Wetland (JBEW; 1990-1992).  Prepared for the Unified Sewerage Agency, Hillsboro, Oregon. SRI/Shapiro, Inc., Portland, Oregon, in association with Luzier Hydrosciences, Portland, Oregon.  November 16, 1994.

U. S. Bureau of Reclamation.  2001.  Biological assessment ofKlamath Project’s continuing operations on the endangered Lost River sucker and shortnose sucker.  Prepared by the Klamath Basin Area Office, BR, Klamath Falls, Oregon.  February 13, 2001.

U. S. Bureau of Reclamation.  2001.  Digital file of end-of-month lake elevations and Basdekas (1997 memorandum), Jim Bryant.  Personal communication with S. Geiger, Shapiro and Associates, Inc. May 15, 2001.

U. S. Environmental Protection Agency.  2000.  Constructed wetlands treatment of municipal wastewaters.  EPA/625/R-99/010  Office of Research and Development, Cincinnati, Ohio.  September 2000

U. S. Fish and Wildlife Service.  2001.  Biological Opinion:  Bureau of Reclamation’s proposed operation of the Klamath Project.  California/Nevadda Operations Ofrfice, Sacramento, California.  April 5, 2001.

Walker,W.  2001.  Development of a phosphorus TMDL for Upper Klamath Lake, Oregon.  Prepared for the Oregon Department of Environmental Quality, Bend, Oregon.  Prepared by W. Walker, Concord, Massachusetts.  March 7, 2001.

Wetzel, Robert.  1975.  Limnology.  W. B. Saunders Company, Philadelphia.

Xue, H., L. Sigg.  1999.  Comparison of the complexation of Cu and Cd by humic and fulvic acids and by ligands observed in lake waters.  Aquatic Geochemistry.  5:313-335.